## Slide 1: Structural determination – 1(B)
Yeou-Guang Tsay, M.D., Ph.D.
Institute of Biochemistry & Molecular Biology Biomedical Industrial Ph.D. Program Biomedical EMBA Program
What properties are examined in IR?

## Slide 2: Spectroscopic analyses of organic compounds
Technique | Electromagnetic radiation | Structure
Infrared spectrometry | Infrared light | Covalent bonds
Ultraviolet spectroscopy | Ultraviolet light | σ–σ*, n–σ*, π–π*, n–π* transitions
Nuclear magnetic resonance spectroscopy | Radio wave | Atomic nuclei in magnetic field
Frequency (ν) in Hz
380 nm
780 nm
Wavelength (λ) in m

## Slide 3: Properties of electromagnetic radiation – Wave-particle duality
Electromagnetic radiation has dual properties.
Wave properties - In homogeneous media, electromagnetic radiation is a transverse wave, meaning that its oscillations are perpendicular to the direction of energy transfer and travel
Wavelength (λ)
Amplitude
C = λ∙ν = 2.998 × 108 m/sec
Frequency (sec-1 = Hz)
Light speed
Particle properties - The particle of light has the name photon, like other particles such as the electron and proton. Thus, a photon is a single quantum of light

## Slide 4
Wavelength (λ)
Frequency (sec-1 = Hz)
The minimum amount of any physical property involved in an interaction. This means that the magnitude of the physical property can take on only discrete values consisting of integer multiples of one quantum.
Quantum (plural: quanta)
A photon, or any other form of electromagnetic radiation, has the quantum of energy (ε) that is in direct proportional to its frequency (ν)
ε = h∙ν
6.62607015 × 10−34 J⋅s
Planck constant
E = NA × ε = 4 × 10−10 ∙ ν (J⋅s/mol)

## Slide 5: Infrared spectroscopy
Wavelength (λ; m)
(ν; sec-1 = Hz)
Frequency
Wavenumber (ṽ; cm-1)
1014
1013
1012
10-6
10-5
10-4
(33)
(333)
(3333)
Energy
4000
3500
2500
3000
2000
1000
500
1500
Transmittance (%)
100
80
60
40
20
0
CH3OH
Near
Far
Frequency
100% at top
What structures absorb the energy in IR?

## Slide 6: The absorption of infrared quanta causes vibration of covalent bonds
Upon absorption of the infrared radiation of a specific frequency, molecules stretch or bend if the frequency of the radiation matches the frequency of the vibration
Symmetric stretching
Antisymmetric stretching
In-plane bending
Out-of-plane bending
How do we interpret the IR spectra?

## Slide 7: Interpret infrared spectra
4000
3500
2500
3000
2000
1000
500
1500
Transmittance (%)
100
80
60
40
20
0
Wavenumber (ṽ; cm-1)
CH3OH
Fingerprint
C=O
C=N
C=C
C≡N
C≡C
O−H
N−H
C−H
Most functional groups have characteristic IR absorption bands that do not change from one compound to another
1500
2850
2000

## Slide 8
C−H
=C−H
≡C−H
C≡C
Φ Ring bonds
C=C
Infrared absorption frequencies in organic chemistry
=C−H
4000
3500
2500
3000
2000
1000
500
1500
C−H
O
=
C=O
C≡N
O−H
(alcohol)
O−H (Carboxylic acid)
NO2
N−H
C=N
NP2, NP3

## Slide 9
4000
3500
2500
3000
2000
1000
500
1500
C−H
=C−H
≡C−H
C≡C
Φ Ring bonds
C=C
Group | Class | Frequency, cm-1 | Signal | Group | Class | Frequency (cm-1) | Signal
C-H | Alkane | 2850-2960 | M | ≡C-H | Alkyne | 3300 | S
=C-H | Alkene | 3020-3100 | M | C≡C | Alkyne | 2100-2260 | M
C=C | Alkene | 1640-1680 | M | =C-H | Arene | 3030 | W
W: weak, M: medium, S: strong |  |  |  | Φ Ring bonds | Arene | 1450-1600 | M
Infrared absorption frequencies of hydrocarbons

2
=C−H
NP2

## Slide 10: IR characteristics in alkane, alkene and alkyne
4000
3500
2500
3000
2000
1000
500
1500
Wavenumber (ṽ; cm-1)
1640-1680
C=C
2100-2260
C≡C
3020-3100
=C-H
3300
≡C-H
CH3(CH2)4CH3
An alkane
CH3(CH2)3CH=CH2
An alkene
CH3(CH2)3C≡CH
An alkyne




Transmittance (%)
80
40
0
80
40
0
80
40
0

2850-2960
-C-H

## Slide 11
4000
3500
2500
3000
2000
1000
500
1500
C−H
=C−H
≡C−H
C≡C
Φ Ring bonds
C=C
Bond | Class | Frequency, cm-1 | Signal | Bond | Class | Frequency (cm-1) | Signal
C-H | Alkane | 2850-2960 | M | ≡C-H | Alkyne | 3300 | S
=C-H | Alkene | 3020-3100 | M | C≡C | Alkyne | 2100-2260 | M
C=C | Alkene | 1640-1680 | M | =C-H | Arene | 3030 | W
W: weak, M: medium, S: strong |  |  |  | Φ Ring bonds | Arene | 1450-1600 | M
Infrared absorption frequencies of hydrocarbons
2
3


1½
=C−H
NP2

## Slide 12: IR characteristics in arenes versus alkene
4000
3500
2500
3000
2000
1000
500
1500
Wavenumber (ṽ; cm-1)
Transmittance (%)
0
0
100
50
0
100
50
100
50
1640-1680
C=C
3020-3100
=C-H
CH3(CH2)3CH=CH2
C6H6 (Benzene)
1450-1600
C=C
1450-1600
C=C
C=C
Φ Ring bonds
Φ Ring bonds




3030
3030



C6H5-CH3 (Toluene)
=C-H
=C-H

## Slide 13: Infrared absorption frequencies of oxygen-containing substances
Bond | Functional class | Frequency cm-1 | Signal | Bond | Class | Frequency cm-1 | Signal
O-H | Alcohol | 3400-3650 | S&B | N-H | Amine | 3300-3500 | M
O-H | Carboxylic acid | 2500-3100 | S&B | C=N | Imine | 1610-1690 | S
=C-H | Aldehyde | 3020-3100 | M | C≡N | Nitrile | 2210-2260 | M
C=O | Aldehyde, ketone, ester, amide and carboxylic acid | 1670-1780 | S | NO2 | Nitro | 1540 | S
 |  |  |  | W: weak, M: medium, S: strong |  |  | 
4000
3500
2500
3000
2000
1000
500
1500
C−H
O
=
C=O
C≡N
O−H
(alcohol)
O−H (Carboxylic acid)
NO2
N−H
C=N
NP3

## Slide 14
Infrared spectroscopy – phenol
H-O stretching
3400~3650 cm-1 (Strong, broad)
4000
3000
2000
1500
1000
500
100
80
60
40
20
Transmittance (%)
Wavenumber
1450-1600
C=C
C=C
Φ Ring bonds





## Slide 15
Infrared spectroscopy – alcohol
Wavenumber
H-O stretching
3400~3650 cm-1 (Strong, broad)
4000
3000
2000
1500
1000
500
100
80
60
40
20
Transmittance (%)

## Slide 16: Infrared absorption frequencies of oxygen-containing substances
Bond | Functional class | Frequency cm-1 | Signal | Bond | Class | Frequency cm-1 | Signal
O-H | Alcohol | 3400-3650 | S&B | N-H | Amine | 3300-3500 | M
O-H | Carboxylic acid | 2500-3100 | S&B | C=N | Imine | 1610-1690 | S
=C-H | Aldehyde | 3020-3100 | M | C≡N | Nitrile | 2210-2260 | M
C=O | Aldehyde, ketone, ester, amide and carboxylic acid | 1670-1780 | S | NO2 | Nitro | 1540 | S
 |  |  |  | W: weak, M: medium, S: strong |  |  | 
4000
3500
2500
3000
2000
1000
500
1500
C−H
O
=
C=O
C≡N
O−H
(alcohol)
O−H (Carboxylic acid)
NO2
N−H
C=N
NP3

## Slide 17: Infrared spectroscopy - aldehyde
Wavenumber
4000
3000
2000
1500
1000
500
100
80
60
40
20
Transmittance (%)
1670-1780
C=C
C=C
Φ Ring bonds


3020-3100 cm-1
C=O

1450-1600

sp2 C-H

## Slide 18: Infrared spectroscopy - ketone
Wavenumber
4000
3000
2000
1500
1000
500
100
80
60
40
20
Transmittance (%)
1670-1780
C=O


## Slide 19
Infrared spectroscopy of alcohols, phenols, aldehydes and ketones
O-H
O-H
C=O
C=O
Φ Ring bonds
Φ Ring bonds
sp2 C-H

## Slide 20: How to use infrared spectroscopy to distinguish two compounds with the same chemical formula C3H6O?
Acetone
CH3COCH3
Prop-2-en-1-ol
H2C=CHCH2OH
vs
1670-1780
1640-1680
3400-3650 (Broad)
4000
3500
2500
3000
2000
1000
500
1500
Wavenumber (ṽ; cm-1)
Transmittance (%)
0
100
50
0
100
50
Prop-2-en-1-ol
Acetone

## Slide 21: How to predict the structure based on infrared spectroscopy?
4000
3500
2500
3000
2000
1000
500
1500
Wavenumber (ṽ; cm-1)
Transmittance (%)
80
40
0
20
60
100
C=O
Strong
Φ Ring bonds
Φ Ring bonds
sp2 C-H
Aldehyde
Aromatic ring
The table will be given in my test. Learn how to find the needed info from the table

## Slide 22: Spectroscopic analyses of organic compounds
Technique | Electromagnetic radiation | Structure
Infrared spectrometry | Infrared light | Covalent bonds
Ultraviolet spectroscopy | Ultraviolet light | σ–σ*, n–σ*, π–π*, n–π* transitions
Nuclear magnetic resonance spectroscopy | Radio wave | Atomic nuclei in magnetic field
Frequency (ν) in Hz
380 nm
780 nm
Wavelength (λ) in m
= S2

## Slide 23: Ultraviolet spectroscopy
Wavelength (λ; m)
(ν; sec-1 = Hz)
Frequency
Absorbance
1.0
0.8
0.6
0.4
0.2
0.0
1016
1015
1014
10-8
10-7
10-6
Energy
200
220
400
Wavelength (nm)
300
240
260
280
320
340
360
380
Ultraviolet
Vis
UV
(Buta-1,3-diene)
λmax = 217 nm
CH2=CH-CH=CH2
0 at bottom
What compounds have a peak in the UV spectrum?
>200 nm
Conjugated diene

## Slide 24: Ultraviolet spectroscopy
Ultraviolet spectroscopy refers to absorption spectroscopy or reflectance spectroscopy in part of the ultraviolet spectral regions. In this region of the electromagnetic spectrum, atoms and molecules undergo electronic transitions. Absorption spectroscopy measures transitions from the ground state to the excited state.
Molecules containing bonding (σ- and π-electrons) or non-bonding electrons (n-electrons) can absorb energy in the form of ultraviolet to excite these electrons to higher anti-bonding molecular orbitals.
The more easily excited the electrons, (i.e. lower energy gap between the HOMO and the LUMO), the longer the wavelength of light it can absorb
What properties are examined in UV-Vis?
Highest Occupied MO
Lowest Unoccupied MO
Energy gap between HOMO and LUMO

## Slide 25: Various HOMO-LUMO transitions leading to ultraviolet absorption
π (bonding)
σ (bonding)
σ* (Antibonding)
π* (Antibonding)
n (nonbonding)
σ–σ* > n–σ* > π–π* > n–π*
NP5
N-, O-

## Slide 26: Ultraviolet spectroscopy of acetone
H3CCCH3
O
=
σ + π
:
:
n
π (bonding)
σ (bonding)
σ* (antibonding)
π* (antibonding)
n (nonbonding)
π–π*
195 nm
275 nm
Weak signal but quite distinct
Absorbance
1.0
0.8
0.6
0.4
0.2
0.0
200
220
Wavelength (nm)
240
260
π–π* transition
n–π* transition
λmax = 275
λmax = 195
What structure can narrow the energy gap between HOMO and LUMO?
n–π*
vs 165 nm for ethene

## Slide 27: π–π* transition for buta-1,3-diene
A conjugated diene
Four 2p atomic orbitals (AO)
Four Ψ molecular orbitals (MO)
Ψ4*
Ψ3*
Ψ2
Ψ1
LUMO
HOMO
Highest occupied
hν
π
π*
Ground state electronic configuration
Excited state electronic configuration
217 nm
UV irradiation
Lowest unoccupied
π
π*
vs ethene 165 nm

## Slide 28: UV absorption in conjugated polyenes
290 nm
258 nm
217 nm
165 nm
Ψ4*
Ψ3*
Ψ2
Ψ1
Buta-1,3- diene
Ψ2*
Ψ1
Ψ3
Ψ2
Ψ1
Ψ4*
Ψ5*
Ψ6*
Ψ3
Ψ2
Ψ1
Ψ4
Ψ7*
Ψ6*
Ψ5*
Ψ8*
Ethene
Hexa-1,3,5- triene
Octa-1,3,5,7- tetraene
HOMO
LUMO
H2C=CH-HC=CH2
H2C=CH-C=O
H3C
Enone
H2C=CH-C=CH2
H3C
All have similar λmax
(220 nm)
(219 nm)
n–π* 320 nm
(217 nm)
As the number of conjugated C=C becomes higher, the energy gap between HOMO and LUMO decreases and the wavelength of absorbed light increases

## Slide 29: UV absorption in cyclic vs linear conjugation
165 nm
Ψ2*
Ψ1
Ethene
258 nm
Ψ4*
Ψ3
Ψ2
Ψ1
Ψ5*
Ψ6*
Hexa-1,3,5- triene
203 nm
.
Antibonding
Bonding
Benzene
Ψ4*
Ψ3
Ψ2
Ψ1
Ψ5*
Ψ6*
Cyclic conjugation may give a peak with λmax > 200 nm in UV spectra as well
HOMO
LUMO

## Slide 30: Colors of organic compounds result from extensive conjugation
As the number of conjugated C=C becomes higher, the energy gap between HOMO and LUMO decreases. When the wavelength of absorbed light is in the range of visible light, the compound should become colored
β-Carotene has λmax = 455 nm. When white light strikes β-carotene, wavelengths in the blue region are absorbed. Thus, the yellow-orange colors are transmitted to our eyes
β-Carotene
Retinol production

## Slide 31: A vitamers in visual cycle
11-cis-Retinol
11-cis-Retinal + opsin
NAD(P)
reductase
Isomerase
NAD(P)
reductase
All-trans-Retinal + opsin
All-trans-Retinol
Isomerase
Rhodopsin
Dark adaptation
hν
Nerve excitation
(From circulation)
hν
11-cis-retinal
In retina
Cell membrane
Outside
Inside
Ion influx
Opsin
Optic nerve transmission
Rhodopsin
Metarhodopsin II
A protein
Metarhodopsin II

## Slide 32: Some structures in visual cycle
All-trans-Retinol
11-cis-Retinal
Rhodopsin
A protein
Imine bond
Metarhodopsin II
hν
Apo-opsin
N-opsin
N-opsin

## Slide 33: Absorbance (A) and molar absorptivity (ε)
Absorbance () is the common logarithm of the ratio of incident () to transmitted () radiant power through a material
Molar absorptivity (ε), or molar extinction coefficient, is a measure of how strongly a chemical species or substance absorbs light at a particular wavelength
Molar concentration
Sample pathlength (cm)